## Slide 1: SCUTTLE Software Guide
revised 2021.07.22
See errors? Inform scuttleProject@gmail.com
Software Architecture
Software best practices
Sensor Communication
Obstacle Avoidance

## Slide 2: Software Architecture
The SCUTTLE robot software has been programmed in Python3 on an embedded Linux platform. Both Beaglebone Blue and Raspberry Pi have been tested successfully. The software has been architected to make a robust starting point for students to create their own autonomous missions. These slides detail the software architecture.
CONTENTS
LANGUAGE
FUTURE OUTLOOK
This guide covers
The parts of each software file
How the programs interact with each other
How the programs interact with hardware
Sensor software vs actuator software
Next Steps: Robotic Operating System 2 (ROS2) is quickly becoming a reliable, versatile software platform for mobile robots. During 2021 the SCUTTLE team will aim to create a new ROS2 version of the software.
See errors? Inform scuttleProject@gmail.com

## Slide 3: Software Architecture – Introduction
data
The blocks in yellow are sensors, and the items in orange are actuators or other outputs. The level-2 blocks in teal are specific to the hardware platform (beagle, pi, etc) and perform communication with the low level devices. The blocks of level2 and above are non-hardware specific.
Each block aside from sensors and actuators represent an individual python program. The purple text indicates what important information is passed between programs and the black arrows indicate (for the most part) what direction the data is flowing. If a level 3 program needs information from another, it must receive the information from the top-level program, in order to maintain the structure of independence in program functions.
This software structure is preferred in order to perform subsystem testing. The data flowing through the top level is minimal and can be replaced with artificial data in the even that a sensor is unavailable.
Sensors
Actuators
programs
[var_A, var_B]
programs
See errors? Inform scuttleProject@gmail.com

## Slide 4: Software Architecture - Overview
Color Key
L1_motors.py
generate 4 signals to output pins
L2_kinematics.py
compute chassis movement
[pwmA, pwmB, pwmC,pwmD]
Wheel Encoders Column
Motor Driver inputs 1,2
Motor Driver inputs 3,4
L2_speed_control.py
generate wheel duty cycle commands
[duty_L,duty_R]
[phiL, phiR]
L1_encoder.py
get the information from encoders
cpu clock
Motor Driver Column
[x_dot,
theta_dot]
Left Encoder 0x40
Right encoder 0x41
Sensors
Level 2 Program (logic-defining)
Level 1 Program (hardware-specific)
Actuators
L3_drive_mt.py
multithreading driving
GamePad controller
L1_gamepad.py get the information from gamepad
[nearest obstacle]
L2_inverse_kinematics.py compute wheel vectors
[target_x_dot,
target_theta_dot]
+14 values
Game Controller Column
[target_phi_dot_L,
target_phi_dot_R]
LIDAR TiM561
L1_lidar.py
get the information from lidar
L2_obstacle.py
compute obstacles
[array of distances & angles]
LIDAR column
L1_text2speech.py
generate audio signals for aux output
analog
audio
Audio Driver
Audio Output Column
[text string]
[target_phi_dot_L,
target_phi_dot_R]
See errors? Inform scuttleProject@gmail.com

## Slide 5: Software Architecture – Overview (continued)
Color Key
ADC
voltage sensor
L1_adc.py
get adc data
L2_onboard.py
compute battery info
[adc
values]
Sensors column
[battery info] or
[temp, press] or
[mpu data]
MPU9250
motion sensor
BMP280
enviro sensor
L1_bmp.py
get bmp data
L1_mpu.py
get mpu data
USB
camera
L1_camera.py get the image from camera
L2_track_target.py
compute steering
[target_x,
target_y, target_radius]
Camera column
[target_x_dot,
target_theta_dot]
Sensors
Code Modules (logic-defining)
code modules (hardware-specific)
Actuators
L1_servo.py
send commands to servos
servo command
Servo 1
Servo Column
Servo 8
…
[mpu
values]
[bmp
values]
myLog.csv
data log
L2_log.py
Data logging column
[data to
be logged]
[array of commands]
servo command
to the L3 program
[strings]
See errors? Inform scuttleProject@gmail.com

## Slide 6: Libraries in use:
Python importing guidelines:
Each file should import the files below it in hierarchy, and not the files above it.
Each file may import non-scuttle libraries as needed (import NumPy, import time, etc.)
If the Level-1 file has imported an external library, it does not need to be imported by the Level-2 file
Libraries Utilized:
BeagleBone Blue Integration:
RCPY for communicating with MPU9250 & commanding motor drivers
Adafruit GPIO for I2C Communication
BMP280 for communicating with the onboard bmp280 sensor.
Raspberry Pi integration:
pysicktim for accessing LIDAR data
gpiozero for controlling GPIO pins.
Common Libraries
os for making shell commands via python code.
time for keeping track of time
threading for performing multithreading
NumPy for performing math operations
Fastlogging for generating log files
pygame for accessing gamepad controller data
cayenne.client for sending MQTT messages
smbus2 for accessing i2c bus through python commands
See errors? Inform scuttleProject@gmail.com

## Slide 7: Libraries Matrix
Lib | Beaglebone Blue | Raspberry Pi 3B+ and 4 | Jetson Nano [Under development]
Time | ✔ | ✔ | ✔
Threading | ✔ | ✔ | ✔
numpy | ✔ | ✔ | ✔
pygame | ✔ | ✔ | 
fastlogging | ✔ | ✔ | ✔
Cayenne.client | ✔ | ✔ | 
PySICKtim |  | ✔ | 
GPIOZERO |  | ✔ | 
RCPY | ✔ |  | 
ADAFRUIT GPIO | ✔ |  | 
BMP280 | ✔ |  | 
See errors? Inform scuttleProject@gmail.com

## Slide 8: Outline of an L1 Program
Explanation of the purpose
Import internal programs (if applicable)
Import external programs (aka libraries). Take actions for initializations of objects or global variables.
Define functions. In some cases, make functions that combine other functions in sequence.
Offer a simplified, minimal loop for testing the code.
All files follow this outline when possible. The level-1 programs are most suited to this outline.
See errors? Inform scuttleProject@gmail.com

## Slide 9: Guidelines for Levels
Importing
Files & Libraries
Sensor
actual hardware
L1_program.py
get the data from sensor
L2_program.py
compute parameters from L1 data
[raw data
subset]
[data relevant
to the mission]
Only import L1 programs directly below. Do not import L3 program. As needed, import external libraries.
Do not import L2 or L3 programs. As needed, import external libraries.
Testing
Code and Hardware
This file has a loop to test the whole group (L1 + L2 + sensor).
This file has a loop to test sensor function.
pass data to L3
[raw sensor
data]
See errors? Inform scuttleProject@gmail.com

## Slide 10: Multi-threading Purpose
When?
Do What?
Threading offers better control over timing of code execution.
Each thread should contain actions that are related and that should be executed within a specific time window.
The user should avoid passing data between threads because it reduces robustness. Instead, call the level 2 program as needed in each thread, even if you need to communicate with the same device (ie, retrieve gamepad commands for driving and retrieve in parallel for speaking commands)
Thread 1 (driving)
Thread 2 (obstacle detect)
Drive the robot
After sampling the controller
AND
Log the speed
After sending drive command
Indicate obstacles using speaker
when obstacle is detected by lidar
Thread 3 (speaking)
10ms cylcle
20ms cylcle
speak via speaker
user presses button
5ms cylcle
See errors? Inform scuttleProject@gmail.com

## Slide 11: Software Architecture: Sensors vs Actuators
Actuators
Actuator
actual hardware
L1_program.py
send commands to actuator
L2_program.py
compute commands for L1 program
[message for actuator]
[message from
the mission]
pass command from L3
[message for
L1 program]
Sensors
Sensor
actual hardware
L1_program.py
get the data from sensor
L2_program.py
compute parameters from L1 data
[raw data
subset]
[data relevant
to the mission]
pass data to L3
[raw sensor
data]
Sensor and Actuators have the same architecture except for data direction.
For sensors, the data is generated at the hardware and sent UP.
For actuators, the data is generated at the top and sent DOWN to hardware.
Some sensors and actuators have feedback and preset commands, so data may flow both ways.
See errors? Inform scuttleProject@gmail.com

## Slide 12: Software Architecture: Modularity & Robustness
Sensor
actual hardware
L1_program.py
get the data from sensor
L2_program.py
compute parameters from L1 data
[raw data
subset]
[data relevant
to the mission]
Send and receives data in the format that is “universal” or standardized.
If there is a hardware change, this program does not need to change
If the driving strategy changes, this program may change
The job of L1 program is to convert the data into the desired format.
If there is a hardware change, only these items need to be updated.
If the driving strategy changes, these items do not change.
pass data to L3
[raw sensor
data]
See errors? Inform scuttleProject@gmail.com

## Slide 13: Level 1: logging
myErrorLog.csv
data log
Info retrieved for text2speech
functions:
logSpeeds()
logError()
logNewDataType()
myLogMsg.txt
data log
+ new log.csv
created data log
L1_log.py
compute parameters from L1 data
info for nodeRed charts
Rather than interacting with hardware, the L1_log program interacts with other python files. It acts as a sensor in that it retrieves recorded data and it acts as an actuator in that it can receive data and perform an action with it (store it in a file).
L1_log.py program was initially designated as level2, but is being set as L1 going forward (2020.11)
See errors? Inform scuttleProject@gmail.com

## Slide 14: Multithreading example
L1_motors.py
generate 4 signals to output pins
L2_kinematics.py
compute chassis movement
[pwmA, pwmB, pwmC,pwmD]
Wheel Encoders Column
Motor Driver inputs 1,2
Motor Driver inputs 3,4
L2_speed_control.py
generate wheel duty cycle commands
[duty_L,duty_R]
[phiL, phiR]
L1_encoder.py
get the information from encoders
cpu clock
Motor Driver Column
[x_dot,
theta_dot]
Left Encoder 0x40
Right encoder 0x41
Sensors
Level 2 Program (logic-defining)
Color Key
Level 1 Program (hardware-specific)
Actuators
L3_drive_mt.py
multithreading driving
GamePad controller
L1_gamepad.py get the information from gamepad
L2_inverse_kinematics.py compute wheel vectors
[target_x_dot,
target_theta_dot]
+14 values
Game Controller Column
[target_phi_dot_L,
target_phi_dot_R]
L1_text2speech.py
generate audio signals for aux output
analog
audio
Audio Driver
Audio Output Column
[text string]
[target_phi_dot_L,
target_phi_dot_R]
mpu sensor
compass driver in RCPY Lib
L2_heading.py
compute steering
[tcompass_x,
tcompass_y]
Compass column
[heading (degrees)]
L3_tellHeading.py
declare robot heading on speaker
See errors? Inform scuttleProject@gmail.com

## Slide 15: Color Tracking Example
Color Key
L2_track_target.py
Finds color target in range
Camera Column
[image]
L1_camera.py
Get image from USB camera
Sensors
Level 2 Program (logic-defining)
Level 1 Program (hardware-specific)
Actuators
L3_follow.py
Object Following
L1_gamepad.py
Not used
[target speeds]
L2_inverse_kinematics.py
Compute wheel vectors
Kinematics Column
L1_motor.py
Generate signals to output pins
L2_speed_control.py
Converts speeds into duty cycles
[duty cycles]
Motor Driver column
[target_phi_dot_L,
target_phi_dot_R]
See errors? Inform scuttleProject@gmail.com
Wide-Angle Camera
[pwmA, pwmB, pwmC,pwmD]
Motor Driver inputs 1,2
Motor Driver inputs 3,4
[target offset from center]
[target offset
[-1,1] ]

## Slide 16: Absolute Orientation
SCUTTLE has a compass for orientation
  The compass is nothing but a 3-axis magnetometer
  Encoders can provide relative orientation
  Compass is required for global orientation
The compass is embedded in the IMU (MPU-9250)
  It has 3 sensors oriented in the indicated directions
  L1_mpu.py accesses the magnetometer
  Each magnetometer requires calibration
global coordinate frame
x’
Y’
Remember: Theta is defined as scuttle’s chassis x-vector minus the global x-vector
ϴc
x
this theta is positive
See errors? Inform scuttleProject@gmail.com

## Slide 17: Magnetometer Behavior
An axis is at its MAXIMUM when it is aligned NORTH
The axis is at its MINIMUM when it is opposing NORTH
After calibration, we can achieve the behavior below
Values Desired by Direction
Using X axis for example:
xc = 0
xc = 1
xc = 0
xc = -1
2) Using the following equation, re-scale each axis
1) Discover the maximum and minimum values by rotating sensor in a full circle.
Permanent magnets influence the sensor, so calibration must be done on the robot, in position near the motors.
Before Calibration | Min (microtesla) | max (microtesla)
X | -15 | 38
Y | -22 | 20
AfterCalibration | Min (ratio to max) | max (ratio to max)
X | -1 | 1
Y | -1 | 1
(magnetic north)
See errors? Inform scuttleProject@gmail.com

## Slide 18: Determining Absolute Orientation
X and Y axes are sufficient information to give heading.
  Z axis returns zero if scuttle sits flat
Theta is defined as rotation of SCUTTLE from the global coordinate frame, or y-prime
  positive theta means SCUTTLE is turned left from north
  We can define NORTH as the y-axis of the global coordinate frame
Theta is positive when scuttle points west
Theta is negative when scuttle points east
Use arctan2(y, x) to return a heading
arctan2 is the "element-wise arc tangent of y/x choosing the quadrant correctly."
ATAN2(0.91, 0.42) returns 25 degrees
Example:
y = 0.91
x = 0.42
y-prime
y is pointed strongly north
X is pointed weakly north
both axes return positive values
See errors? Inform scuttleProject@gmail.com

## Slide 19: Speeds Tuning
Vmax = 0.4m/s (measured by wheel speed)
v = ω *r
ωmax, motor pulley = 19.5 rad/s
ωmax, wheel= 9.75 rad/s
With 1 wheel stopped and 1 wheel moving:
  (where L = wheelbase)
max, chassis= 1.98 rad/s (0.32 turns/sec)
These are general performance characteristics you can expect when using the standard SCUTTLE hardware:
Nominal conditions:
Battery: 11.5 volts OC
Motors: equipped with standard 200 rpm gearbox
Wheels: 83mm diameter urethane wheels
Pulleys: motor = 15 teeth, wheel = 30 teeth
Wheelbase: 405mm
See errors? Inform scuttleProject@gmail.com

## Slide 20: Speeds Tuning
Vmax = 0.4m/s (measured by wheel speed)
v = ω *r
ωmax, motor pulley = 19.5 rad/s
ωmax, wheel= 9.75 rad/s
With 1 wheel stopped and 1 wheel moving:
  (where L = wheelbase)
max, chassis= 1.98 rad/s (0.32 turns/sec)
These are general performance characteristics you can expect when using the standard SCUTTLE hardware:
Nominal conditions:
Battery: 11.5 volts OC
Motors: equipped with standard 200 rpm gearbox
Wheels: 83mm diameter urethane wheels
Pulleys: motor = 15 teeth, wheel = 30 teeth
Wheelbase: 405mm
See errors? Inform scuttleProject@gmail.com

## Slide 21: SCUTTLE Driving
The left joystick operates the robot wheels
The forward/backward axis will request a speed
  (A.K.A movement in x)
The left/right axis will request an angular velocity
  (A.K.A movement in theta)
requests
requests
axis 1+
axis 3+
axis 0+
B2
B1
B0
B3
axis 2+
B4
B5
B10
B11
B8
B9
select proper mode
Gamepad Controls Mapping
Trigger: B6
Trigger: B7
Move | Theta_dot (rad/s) | X_dot (m/s) | Phi_dot
max | 1.99 | 0.4 | 9.75
Given a measured max forward velocity of 0.4m/s, the other maximums are calculated.
See errors? Inform scuttleProject@gmail.com

## Slide 22: SCUTTLE Movement Example
right turn on joystick
outputs positive value on axis_1
interpret as negative theta movement
performs
POSTIVE phi_dot_l and NEGATIVE phi_dot_R
USER SAYS
GAMEPAD SAYS
KINEMATICS SAYS
KINEMATICS SAYS
MOTOR PROGRAM SAYS
performs
POSTIVE differential on NEGATIVE phi_dot_R
Move | Theta_dot | X_dot | Duty_r | Duty_l
Fwd | 0 | 1 | 1 | 1
Rev | 0 | -1 | -1 | -1
right | -1 | 0 | -1 | 1
left | +1 | 0 | 1 | -1
See errors? Inform scuttleProject@gmail.com

## Slide 23: SCUTTLE Color Tracking
Wide-Angle
Camera
150˚
Center
Threshold
Radius=15 pixels
Radius=20 pixels
Wide-Angle
Camera
1) SCUTTLE turns until the target is detected within the threshold
2) After the target is in the center range, SCUTTLE drives forward or backwards to reach a target radius, in pixels.
Drive forward
Drive backward

## Slide 24: LIDAR Concept of Operation
ANATOMY
Lidar systems have a rotating sensor collecting multiple measurements to measure in a 2D plane. (Some have 3D, by other methods).
METHOD
Lidar emits a beam of light and receives the reflection. distance is based on Time of Flight concept.
POWER
TiM561 uses about 2.1 watts during operation, mainly due to driving the motor and driving a strong IR emitter diode.
FAILURE MODES
Just like light, a Lidar beam can be absorbed by very dark objects and can be mis-directed by highly reflective objects which are non-perpendicular to the beam.
DATA QUALITY
The lidar has variable resolution in a sense! 0.33 degrees offers 5mm point spacing at a 1m distance, and at 10 meters, 50mm point spacing.
APPROPRIATE USE
To be successful in using the device, you need to see the datasheet to understand the parameters of your device.
d
maximum range
Lidar Device
Wall
See errors? Inform scuttleProject@gmail.com

## Slide 25: LIDAR – measuring a point
P1 is the location of the lidar.
The points will be initially measured from lidar and returned as pairs given by:
[d (mm), α (degrees)]
Python’s numpy library performs math in radians. It is easy to convert back and forth but you must be aware of your units.
Obstacle of Interest
P2
d
dx
dy
LIDAR location
P1
α
P0
Center of Wheelbase
See errors? Inform scuttleProject@gmail.com

## Slide 26: Software For LIDAR
Sensors
Level 2 Program (logic-defining)
Color Key
Level 1 Program (hardware-specific)
Actuators
Lab8Template.py
Get the P2 vector & send to nodeRed
[nearest obstacle vector]
LIDAR TiM561
L1_lidar.py
get the information from lidar
L2_vector.py
compute obstacles
[array of distances & angles] (54x2)
LIDAR column
Key Points:
Software is using the numPy library to handle vectors and matrices. numPy computation is faster than raw python and requires proper syntax.
Lidar scan frequency: 15hz, so you cannot get new measurements faster than 66ms.
L1_lidar.py returns 54 measurements by default and can return over 800 single points if desired, for more resolution.
TiM561 LIDAR returns distances in meters. Distances under 16mm are returned as error codes in case of poor reflection or other problem for a given measurement.
L2_vector.py can manipulate measurements, with functions such as returning the nearest point, combining cartesian vectors, and converting vectors from polar to Cartesian coordinates.
See errors? Inform scuttleProject@gmail.com

## Slide 27: Global Location of Obstacle
Determine the global location of an obstacle:
You must add vector r0 and vector r02
First, your vector r02 must be generated using knowledge of the location of the LIDAR on the robot.
global coordinate frame
x’
y’
r0
P0
Where is the obstacle located in the room?
r0-2
P2
P1
vector r02
is not given automatically.
See errors? Inform scuttleProject@gmail.com

## Slide 28: Global Location of Obstacle
Determine the global location of an obstacle:
Lidar is located at positive 254mm in the x-direction on the robot.
The lidar beam is 166 mm above the floor.
See errors? Inform scuttleProject@gmail.com

## Slide 29: Obstacle Avoidance by LIDAR
One method to avoid obstacles is to generate an imaginary spring which pushes on your robot and depends on the nearest obstacle.
Dy is the y-component of distance d
Dx is the x-component of distance d
Wall
P1
P2
d
dx
dy
α
See errors? Inform scuttleProject@gmail.com

## Slide 30: Obstacle Avoidance by LIDAR
Strategy:
The obstacle avoidance feature will try to detect the nearest objects to the robot and apply an “invisible force” to prevent the robot from crashing. The force is intended to act like a spring which is anchored to the nearest obstacle and pushes the robot at a point on the body, referred to as P1.
Wall
P1
P2
d
The obstacle avoidance only deals with the body-fixed frame
Define P1 as a point of interest on our robot.
P2 is assigned to the nearest point detected by the LIDAR scan.
d is the distance between point 1 and point 2
We would like to handle all of these variables in:
  body-fixed frame
  Cartesian coordinates
P0
See errors? Inform scuttleProject@gmail.com

## Slide 31: Obstacle Avoidance – influence on velocity (translational and angular)
If P2 is detected straight ahead, the force influences velocity
If P2 is detected at the side, the force influences steering
If P2 is detected at an angle, the force will influence both
P2
LIDAR location
P2
P2
See errors? Inform scuttleProject@gmail.com

## Slide 32: Obstacle Avoidance – Variable Force
If d is large, the force is low
If d is small, the force is high
If d is larger than dmax, the force is absent
P2
large
force
small
force
P1
See errors? Inform scuttleProject@gmail.com

## Slide 33: Quick Dive – Barometric Pressure
COLLEGE STATION 4-DAY CHANGE
delta in pressure is 30.09-29.58 “Hg  0.51” Hg
delta pressure = 1.73kPa
Historic weather at timeanddate.com
STANDARD PRESSURE CALCULATIONS
sea level std pressure: 101.3kPa
pressure at 1000ft: 97.7kPa
delta pressure = 3.6kPa
elevation change represented by 1kPa = 278ft
What the Barometric pressure will tell you:
1.73kPa change in pressure will represent 480ft altitude change.
See errors? Inform scuttleProject@gmail.com

## Slide 34: Speed Control
This slide is dedicated to describing the wheel speed measurements and calculation of variables for speed control.
Nominal conditions:
Battery: 11.5 volts, open circuit
Motors: equipped with standard 200 rpm gearbox
Wheels: 83mm diameter urethane wheels
Pulleys: motor = 15 teeth, wheel = 30 teeth
See errors? Inform scuttleProject@gmail.com
Update Shaft positions (take reading)
Get Wheel Increments
Update Phis
Update PhiDots
Chassis displacement
Measure position
Capture time
Just math
Integrate the wheel positions
Take derivatives
Update latest wheelspeeds
Chassis speeds
Compute the displacement in theta and x
Take derivative of last movements w.r.t. change in time since last sample.
10hz is sufficient

## Slide 35: Further Reading
https://en.wikipedia.org/wiki/Holonomic_(robotics)
Connector types
http://dangerousprototypes.com/blog/2017/06/22/dirty-cables-whats-in-that-pile/
See errors? Inform scuttleProject@gmail.com